A List of Components

Adder

(Complicated Adder)

\

1. AND gate (x7)
2. OR gate (x2)
3. Inverter (x3)

(NOR logic)

1. NOR gate (x9)

(XOR logic)

1. XOR gate (x2)
2. NAND gate (x3)

x to n Decoder

1. x inverters
2. 2n and gates
(control lines?)

2^n to n Multiplexor

1. n to 2^n decoder
2. n AND gates
3. 1 OR gate
(control lines?)
1 bit MIPS ALU

1. Inverter (x2)
2. 1-2 Multiplexor (x2)
3. Adder (x1)
4. AND gate (x1)
5. OR gate (x1)
6. 2-4 Multiplexor (x1)
(control lines)
32-bit MIPS ALU

1. 1-bit MIPS ALU (x31)
2. 1-bit MIPS ALU with
   overflow detection and
   set output (x1)
3. OR gate (x1)
4. inverter (x1)
32-bit Register

1. Edge-triggered
    Flip-flop (x32)
2^n-Register File

1. Register (x 2^n)
2. n to 2^n
    Decoder (x1)
3. n to 2^n
    Multiplexor (x1)
4. AND gate (x n)
Control Component

The truth table for the control component follows:

	Signal Name:	R-format	lw	sw	beq
Inputs:	Op5	0	1	1	0
	Op4	0	0	0	0
	Op3	0	0	1	0
	Op2	0	0	0	1
	Op1	0	1	1	0
	Op0	0	1	1	0
Outputs:	RegDest	1	0	X	X
	ALUSrc	0	1	1	0
	MemToReg	0	1	X	X
	RegWrite	1	1	0	0
	MemRead	0	1	0	0
	MemWrite	0	0	1	0
	Branch	0	0	0	1
	ALUOp1	1	0	0	0
	ALUOp0	0	0	0	1

The following are boolean conjunctions for the Outputs in the above table:

RegDest = ¬Op0 · ¬Op1 · ¬Op2 · ¬Op3 · ¬Op4 · ¬Op5
AluSrc = Op0 · Op1 · ¬Op2 · ¬Op4 · Op5
MemToReg = Op0 · Op1 · ¬Op2 · ¬Op3 · ¬Op4 · Op5
RegWrite = ¬Op2 · ¬Op3 · ¬Op4
MemRead = Op0 · Op1 · ¬Op2 · ¬Op3 · ¬Op4 · Op5
MemWrite = Op0 · Op1 · ¬Op2 · Op3 · ¬Op4 · Op5
Branch = ¬Op0 · ¬Op1 · Op2 · ¬Op3 · ¬Op4 · ¬Op5
ALUOp1 = ¬Op0 · ¬Op1 · ¬Op2 · ¬Op3 · ¬Op4 · ¬Op5
ALUOp0 = ¬Op0 · ¬Op1 · Op2 · ¬Op3 · ¬Op4 · ¬Op5

It is helpful to notice here the following equivalences:
1. RegDest = ALUOp1
2. Branch = ALUOp0
3. MemToReg = MemRead

Control Component (Cont'd)

In the following diagram, the following conjunctions were “anded” together to simplify the diagram by reducing the number of wires drawn:
1. ¬Op0 · ¬Op1
2. Op0 · Op1
3. ¬Op2 · ¬Op3 · ¬Op4
4. ¬Op2 · ¬Op4

D Flip-Flop

1. D Latch (x2, i.e. - slave and master)
 (Wires)

D Latch

1. AND Gate (x 2)
2. OR Gate (x2)
3. Inverter (x2)
(Wires)